## Slide 1: Multipole Analysis of Electromagnetic Scattering
COMSOL

## Slide 2: Multipole Expansion
The field scattered by a particle, regardless of the particle’s geometrical shape or composition, can always be expressed through the multipole expansion. The expression for the electric field reads (see Ref. 1):
The vector functions

## Slide 3: Multipole Expansion
and
generate a complete basis, where each function describes the field created by a unique multipole.

## Slide 4: Multipole Coefficients
The coefficients aE(l,m) and aM(l,m) characterize the scatterer as they reveal the electric and magnetic excitations in it.
The integer l describes the order of the multipole (dipole, quadrupole, …), whereas the subscripts E and M distinguish between electric and magnetic multipoles. The integer m describes the amount of the z-component of angular momentum that is carried per photon.

## Slide 5: Multipole Coefficients
For optical scatterers, the source of the scattered field is the scattering current density
where eh is the permittivity of the host medium and E(r) is the total field.
The multipole coefficients can be extracted from the scattering current density, using volume integrals over the whole space (see Ref. 2).

## Slide 6: Mie Scattering
Scattering of a plane wave by a spherical particle.
Analytical solution exists as an expansion, in which the coefficients are called Mie coefficients.
MATLAB code (see Ref. 3) exists for computing the Mie coefficients (al and bl).
The Mie expansion is a special case of the Multipole expansion, obtained by setting
  all coefficients to zero, if not |m| = 1
  aE(l,-1) = -aE(l,1)
  aM(l,-1) = aM(l,1)
Connection between the remaining multipole coefficients and the Mie coefficients is
  aE(l,1) = -al
  aM(l,1) = -bl

## Slide 7: COMSOL Implementation
Equations for extracting aE(l,1) and aM(l,1) are implemented in COMSOL using functions and variables
Implementation can be added to any scattering model
Also applicable to periodic systems

## Slide 8: Associated Legendre Polynomials
Rodrigues' formula is used for calculating the associated Legendre polynomials Plm(cosθ)

## Slide 9: Associated Legendre Polynomials
Associated Legendre Polynomial

## Slide 10: Angular Functions
Function tau

## Slide 11: Angular Functions
Function pi

## Slide 12: Coefficient O
Coefficient O

## Slide 13: Multipole Variables
Calculation of aE(l,1) and aM(l,1)
Defined under Component 1 > Definitions

## Slide 14: Mie Benchmark
Mie scattering as a benchmark
  600 nm vacuum wavelength
  Au sphere of 100 nm radius
  Host medium with a refractive index of 1.5
Numerical results are compared to Mie coefficients evaluated in MATLAB
Note: COMSOL uses exp(+jωt) convention, which is handled by setting the imaginary unit i→−j in the equations of this presentation. Complex-conjugation of obtained multipole coefficients returns to exp(-jωt) convention.

## Slide 15: Benchmark Results
Electric Multipole Coefficients |  |  |  |  |  |  | 
l | m=-3, ae (1) | m=-2, ae (1) | m=-1, ae (1) | m=0, ae (1) | m=1, ae (1) | m=2, ae (1) | m=3, ae (1)
1 | 0 | 0 | 0.93538 + 0.082177i | 3.8439E-5 + 2.6268E-5i | -0.93537 - 0.082191i | 0 | 0
2 | 0 | -4.4753E-5 - 7.4743E-6i | 0.70154 + 0.21893i | -8.3438E-6 + 4.0457E-5i | -0.70154 - 0.21893i | 2.3403E-5 + 3.7582E-5i | 0
3 | -5.2441E-6 - 9.8016E-6i | -1.9776E-5 - 7.0469E-6i | 0.0075631 + 0.038522i | -1.74E-6 - 2.6072E-6i | -0.0075571 - 0.038524i | 1.804E-5 - 6.096E-6i | -1.3288E-5 + 5.1912E-6i

## Slide 16: Benchmark Results
Magnetic Multipole Coefficients |  |  |  |  |  |  | 
l | m=-3, am (1) | m=-2, am (1) | m=-1, am (1) | m=0, am (1) | m=1, am (1) | m=2, am (1) | m=3, am (1)
1 | 0 | 0 | -0.094182 + 0.26713i | 1.3235E-6 + 1.2755E-6i | -0.094186 + 0.26714i | 0 | 0
2 | 0 | 5.0097E-7 + 4.0868E-7i | -0.0037616 + 0.034094i | 2.9986E-6 + 4.3089E-7i | -0.0037614 + 0.034094i | 1.4535E-6 - 1.4479E-6i | 0
3 | -2.1472E-7 + 9.8539E-8i | -8.4862E-8 - 2.0176E-7i | -1.7064E-4 + 0.001774i | -2.7469E-8 - 2.8486E-7i | -1.7058E-4 + 0.0017741i | 9.7061E-8 - 1.446E-7i | 3.4911E-7 - 3.5377E-7i

## Slide 17: Comparison to Reference Values
Conjugate and negate the values in the m = 1 column to get values according to the exp(-jω t) convention

## Slide 18: Comparison to Reference Values
Mie Coefficients |  |  | 
l | m | -conj(ae) (1) | -conj(am) (1)
1 | 1 | 0.93537 - 0.082191i | 0.094186 + 0.26714i
2 | 1 | 0.70154 - 0.21893i | 0.0037614 + 0.034094i
3 | 1 | 0.0075571 - 0.038524i | 1.7058E-4 + 0.0017741i

## Slide 19: Reference Values
Reference Values, using exp(-jω t) convention
Reference Values |  | 
l | alpha_l | beta_l
1 | 0.9350 - 0.0826i | 0.0941 + 0.2671i
2 | 0.7003 - 0.2209i | 0.0038 + 0.0341i
3 | 0.0075 - 0.0384i | 0.0002 + 0.0018i
COMSOL values and reference values agree well

## Slide 20: Cross Sections
Scattering cross setion:
Extinction cross setion:

## Slide 21: Cross Sections
Interaction Cross Sections |  | 
Integral: Scattering cross section (m^2) | Integral: Absorption cross section (m^2) | Integral: Extinction cross section (m^2)
1.4268E-13 | 2.7156E-14 | 1.6983E-13

## Slide 22: Cross Sections
Cross Sections from Fields |  |  | 
lambda0 (µm) | Scattering cross section (m^2) | Absorption cross section (m^2) | Extinction cross section (m^2)
0.6 | 1.4201E-13 | 2.7199E-14 | 1.6921E-13
Cross sections from MATLAB code |  | 
Cross Section (m2) | Value | 
Scattering | 1.4252e-13 | 
Absorption | 2.7148e-14 | 
Extinction | 1.6967e-13 | 

## Slide 23: Modal Scattering Cross Section
Only essential contributions from m = -1 and m = 1 terms.

## Slide 24: References
J. D. Jackson, Classical Electrodynamics, 3rd Ed., Wiley, 1999.
P. Grahn, A. Shevchenko, and M. Kaivola, "Electromagnetic multipole theory for optical nanomaterials," New Journal of Physics, vol. 14, no. 9, p. 093033, 2012.
C. Mätzler, "MATLAB functions for Mie scattering and absorption, version 2," in IAP Research Report, University of Bern, 2002.