## Slide 1: Optimization of Liquid Phase Generation by Catalyzed Pyrolysis of PET Plastic Waste
A. Marrero¹, H. Pelaez²
1. Graduate School – Mechanical Engineering, Polytechnic University of Puerto Rico, San Juan Puerto Rico
2. Graduate School – Mechanical Engineering, Polytechnic University of Puerto Rico, San Juan Puerto Rico.
3D porous catalytic reactor used as the reference configuration.
2D axisymmetric model developed for validation.
Chemical Reaction Engineering Module.
Physics: Laminar Flow, Brinkman Equations, Transport of Diluted Species in Porous Catalysts, and Chemistry.
Cases: non-catalytic, Al₂O₃, and NiCl₂.
Catalyst loading: 5 wt% relative to PET.
Governing Model:
Arrhenius reaction kinetics
Convection–diffusion–reaction transport.
Surface reactions and Langmuir adsorption.
PET → HVP (C₇H₆O₂) + LVP (C₂H₆).
[1] Cepeliogullar & Putun, 2013
[2] COMSOL Multiphysics®, 2023
[3] Vijayakumar & Sebastian, 2018
[4] H. Jia et al., 2020.
[5] Kabeyi & Olanrewaju, 2023
Enhancing PET pyrolysis efficiency through catalytic modeling to improve liquid fuel production.
Abstract
Figure 1. COMSOL 3D porous catalytic reactor reference configuration adapted for PET pyrolysis and NiCl₂ modeling [2].
Results:
Non-catalytic case: steady state at 65 s.
Catalytic cases: steady state at ~1260 s.
Catalysts increased concentrations to ~8.0 × 10⁻¹⁵ mol/m³.
NiCl₂ produced ~0.33% higher outlet cross-sectional average concentration than Al₂O₃.
Higher temperature increased concentration; higher velocity decreased it.
Conclusions:
Catalytic cases produced substantially higher predicted HVP/LVP concentrations.
NiCl₂ and Al₂O₃ showed similar predicted performance (<1% difference).
Results are based on a comparative model with simplified catalyst kinetics.
Future work: 3D modeling, liquid-phase yield evaluation, and experimental validation.
Results & Conclusions
Figure 3. Non-catalytic HVP and LVP concentration fields at 65 s and 0.1 m/s.
This study evaluates the potential of a Nickel (II) Chloride (NiCl₂) catalyst toward a target 10% increase in liquid-phase production from PET pyrolysis. A 2D axisymmetric model was developed in COMSOL Multiphysics® to compare non-catalytic, Al₂O₃, and NiCl₂ configurations. NiCl₂ and Al₂O₃ exhibited similar predicted behavior, with less than 1% difference and maximum concentrations of approximately 8.0 × 10⁻¹⁵ mol/m³. The validated parameters will support future implementation in a 3D reactor model and experimental comparison[1].
Introduction & Objectives:
• Plastic waste is a global environmental issue
• PET is widely used and difficult to recycle
• Pyrolysis enables conversion into fuel
• Objective: Evaluate the potential of NiCl₂ toward a target 10% increase in liquid-phase production.
Methodology:
Figure 2. 2D axisymmetric validation models without and with a porous catalytic region.
Figure 4. Catalytic HVP and LVP concentration fields for Al₂O₃ at 1260 s and NiCl₂ at 1259.5 s.
Figure 5. Molar concentration of HVP and LVP versus radius at z = 1.5 m for the non-catalytic, Al₂O₃, and NiCl₂ cases.